## Slide 1
Erosion Simulation: Protecting Our Watersheds
A hands-on exploration of how landscaping choices impact soil erosion and water quality in Florida's waterfront ecosystems.

## Slide 2
Understanding Erosion & Its Impact
What is Soil Erosion?
The process where soil particles are dislodged and transported by water, wind, or other forces
Why It Matters:
Degrades water quality through sedimentation
Reduces soil fertility in landscaped areas
Threatens aquatic habitats and wildlife
Contributes to flooding and property damage
Florida's waterfront ecosystems are particularly vulnerable to erosion damage due to our frequent rainfall and extensive coastlines

## Slide 3
Learning Objectives
1
Identify Erosion Factors
Recognize the causes and effects of soil erosion near waterfronts and how they impact local ecosystems
2
Analyze Slope Impact
Describe and measure how slope angle affects the rate of erosion and water runoff
3
Compare Ground Covers
Evaluate how different materials (bare soil, grass, mulch, rocks) perform in preventing erosion
4
Design Solutions
Apply Florida-Friendly Landscaping principles to create effective erosion control strategies

## Slide 4
Experiment Setup
Materials You'll Need:
Aluminum baking pans or plastic trays
Soil or sand
Ground cover samples: grass sod, mulch, rocks
Books or blocks for creating slopes
Protractor to measure angles
Spray bottles with water and food coloring
Data collection sheets
Work in groups of 3-4 students to create multiple landscape simulations with varying slopes and ground covers

## Slide 5
Conducting the Experiment
Set Up Landscapes
Fill trays with soil and apply different ground covers (bare soil, grass, mulch, rocks). Use books to create various slope angles.
Simulate Rainfall
Use spray bottles with colored water to create consistent "rainfall" on each tray. The dye helps visualize water movement.
Observe & Record
Document erosion patterns, runoff speed, water clarity, and soil displacement for each landscape setup.
Analyze Results
Compare data across different slopes and ground covers to determine which combinations best prevent erosion.

## Slide 6
What to Look For & Measure
Key Observations:
Soil Loss
Estimate amount of displaced soil
Runoff Speed
Time how quickly water moves
Water Turbidity
Note clarity/cloudiness of runoff
Erosion Patterns
Document where and how soil moves
The colored water makes it easier to track water flow paths and identify areas where erosion is most severe

## Slide 7
Florida-Friendly Landscaping Principles
Right Plant, Right Place
Select plants adapted to Florida's climate and specific site conditions that require minimal water, fertilizer and pesticides
Mulch Matters
Apply 2-3 inches of mulch to retain moisture, prevent erosion, and reduce weeds while improving soil structure
Buffer Zones
Create planted areas between lawns and waterways to trap and filter pollutants before they reach water bodies
Manage Yard Waste
Recycle yard waste through composting or proper disposal to prevent nutrient runoff into waterways
Apply these principles when designing your erosion control strategy in the final assessment

## Slide 8
Your Final Challenge
Assessment Options:
Complete lab report analyzing experiment results
Design a landscaping plan for a Florida waterfront property that minimizes erosion
Write a scenario applying Florida-Friendly principles to a real-world erosion problem
Your work will demonstrate your understanding of how landscape design choices impact watershed health and water quality
An IFAS Environmental Science representative may visit our class to discuss real-world applications of these principles and career opportunities in environmental protection!